## Slide 1: SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM
Nastaran Hajinazar1,2,Geraldo F. Oliveira1 , Sven Gregorio1 , Joao Ferreira1 , Nika Mansouri Ghiasi1 , Minesh Patel1 ,Mohammed Alser1 , Saugata Ghose3 , Juan Gómez–Luna1 , Onur Mutlu1
1ETH Zürich, 2Simon Fraser University, 3University of Illinois at Urbana–Champaign
ASPLOS ’21, April 19-23, 2021, Virtual, USA
Prensented by:张梦豪
S211000834

## Slide 2
Motivation:
  Existing processing-using-DRAM proposals either mostly focus on basic bitwise operations and aren't flexible or require significant changes to the DRAM subarray
Observation:
  Shifts can often be eliminated by changing the data-layout, Ambit and RowClone already implement sufficient primitives
Goals:
  A framework that aids the adoption of processing-using-DRAM by efficiently implementing complex operations and providing the flexibility to support new desired operations
Idea:
  Built up complex operations from basic bitwise primitives by offloading scheduling to a separate SIMDRAM control unit
Evaluation:
  Very low area cost (0.2% of a modern CPU)
  Throughput analysis shows that SIMDRAM outperforms both CPUs/GPUs by 88x/ 5.8x respectively
  257x/31x/2.6x more energy efficient than CPU/GPU/Ambit
Executive Summary

## Slide 3: Outline
1. Processing-using-DRAM
2. Background
4. System Integration
3. SIMDRAM
5. Evaluation
6. Conclusion
  SIMDRAM Framework
  Processing-using-DRAM Substrate

## Slide 4: Data Movement Bottleneck
Memory
channel
Main Memory
(DRAM)
Computing Unit
(CPU, GPU, FPGA, Accelerators)
Data movement is a major bottleneck
Bandwidth-limited and power-hungry memory channel
More than 60% of the total system energy
is spent on data movement
Notes: 1. Processing-using-DRAM

## Slide 5: Problem
Data Movement between memory and CPU is slow and inefficient
  Modern applications can be very data intensive, doing computations on large amounts of data can be very slow.
  A lot of computation involves applying data-parallel operations to large amounts of data.
    Traditional SIMD speeds up processing in the CPU, but memory movement overhead still exists.
    Existing Processing-using-DRAM proposals mostly support bitwise operations. Real-world kernels are more complicated, chaining these primitives can be the bottleneck.

## Slide 6: Processing-using-Memory (PuM)
PuM: Exploits analog operation principles of the memory circuitry to perform computation
  Ambit, an Accelerator-in-Memory for bulk bitwise operations. (the first)
  Leverages the large internal bandwidth and parallelism available inside the memory arrays
    Simple logical operations (e.g., AND, OR, XOR)
    More complex operations (e.g., addition, multiplication)

## Slide 7: Inside a DRAM Chip
Access
Transistor
Storage
Capacitor
Bitline
Wordline
Wordline
Bitline
Subarray
(2D Array of DRAM Cells)
Sense Amplifiers
DRAM Module
DRAM Chips
DRAM Bank
DRAM Cells
Row Buffer
Notes: 2. Background

## Slide 8: Ambit: Subarray Organization
Sense amplifiers
Compute rows
Control rows
Data rows
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
Regular
row decoder
Compute
row decoder
Address A
DRAM subarray

## Slide 9: Goal
SIMDRAM: An end-to-end processing-using-DRAM framework that provides the programming interface, the ISA, and the hardware support for:
  Efficiently computing complex operations in DRAM
  Providing the ability to implement arbitrary operations as required
  Using an in-DRAM massively-parallel SIMD substrate that requires minimal changes to DRAM architecture
Notes: 3. SIMDRAM

## Slide 10: SIMDRAM: PuM Substrate
SIMDRAM framework is built around a DRAM substrate that enables two techniques:
(1) Vertical data layout
4-bit element size
Row Decoder
most significant bit (MSB)
least significant bit (LSB)
A
B
Cout
Cin
MAJ
(2) Majority-based computation
Pros compared to the conventional horizontal layout:
Implicit shift operation
Massive parallelism
Cout= AB + ACin + BCin
Pros compared to AND/OR/NOT-based computation:
Higher performance
Higher throughput
Lower energy consumption

## Slide 11: SIMDRAM Framework
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
New SIMDRAM Program
Program
Notes: SIMDRAM Framework

## Slide 12
Step 1: Naive MAJ/NOT Implementation
A
B
Cin
Cout
Part 1
MAJ
0
B
Cin
Cout
MAJ
MAJ
MAJ
A
0
1
1
A
B
C
A
B
C
output is “1” only when A = B = “1”
  output is “0” only when A = B = “0”
Naively converting AND/OR/NOT-implementation to MAJ/NOT-implementation leads to an unoptimized circuit
MAJ
A
B
C
0
MAJ
A
B
C
1

## Slide 13
Step 1: Efficient MAJ/NOT Implementation
Part 2
Step 1 generates an optimized
MAJ/NOT-implementation of the desired operation
A
B
Cout
Cin
MAJ
Greedy
optimization
algorithm
MAJ
0
B
Cin
Cout
MAJ
MAJ
MAJ
A
0
1
1

## Slide 14: Step 2: µProgram Generation
µProgram: A series of microarchitectural operations (e.g., ACT/PRE) that SIMDRAM uses to execute SIMDRAM operation in DRAM
Goal of Step 2: To generate the µProgram that executes the desired SIMDRAM operation in DRAM
  Allocate DRAM rows to the operands
  Generate µProgram

## Slide 15: Step 3: µProgram Execution
SIMDRAM control unit: handles the execution of the µProgram at runtime
Upon receiving a bbop instruction, the control unit:
  Loads the µProgram corresponding to SIMDRAM operation
  Issues the sequence of DRAM commands (ACT/PRE) stored in the µProgram to SIMDRAM subarrays to perform the in-DRAM operation
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
foo () {
bbop_new
}
Program
Control Unit
18
ACT/PRE
SIMDRAM Output
Instruction result
in memory
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done

## Slide 16: SIMDRAM control unit:
…
…
Op 0
Op 63
Op 62
1024
Program
Scratchpad
+1
bbop_op
/
…
Op 0
Op 1
Op 63
PC
16
Op Proccessing
FSM
branch
target
AAP/AP
Op Memory
shift
amount
1
size
dst, src_1, src_2, n
Program
Op
decrement
is_zero
reg dst.
reg src.
1024
Loop
Counter
bbop
FIFO
Register
Addressing Unit
Register File
…
Op 0
Op 63
Op 62
…
Op 0
Op 63
Op 62
From Program
Memory
From
CPU
To Memory
Controller
2
3
4
5
6
7
Notes: Set index of Scratchpad to bbop operand (?)
Write number of iterations into loop counter (= data elements / DRAM row size)
uProg is loaded from Scratchpad into μOp Memory
The Program can be executed one μOp at a time
  μOp is fetched from μOp memory, indexed by the μPC
  Which μRegisters are needed?
    B0-B17 → uReg Addressing Unit generates DRAM addresses
    B18-B31 → The uReg File provides values
uOp Processing FSM executes the uOp
If done loop counter is decremented
  base source and destination addresses are shifted
  resets μPC
  if loop counter = 0 next bbop is executed

## Slide 17: Transposing Data
SIMDRAM operates on vertically-laid-out data
Other system components expect data to be laid out horizontally
Challenging to share data between SIMDRAM and CPU
Notes: 4. System Integration

## Slide 18: Transposition Unit
Last–Level Cache
Transposition Unit
Memory Controller
Object Tracker (OT)
Fetch Unit
Vertical → Horizontal
Transpose
Transpose Buffer
Store Unit
Horizontal → Vertical
Transpose
Transpose Buffer
Transforms the data layout from horizontal to vertical, and vice versa

## Slide 19: Programming interface
ISA
C Code
  Two envisioned ways to use the API:
    Manually where the programmer directly writes SIMDRAM primitives.
      bbop_trsp_init(A, size, elem_size)...
    Automatically using compiler optimizations
      Future work

## Slide 20: Programming interface

## Slide 21: More in the Paper
Efficiently transposing data
Programming interface
Handling page faults, address translation, coherence, and interrupts
Handling limited subarray size
Security implications
Limitations of our framework

## Slide 22: Methodology: Experimental Setup
Simulator: gem5
Baselines:
  A multi-core CPU (Intel Skylake)
  A high-end GPU (NVidia Titan V)
  Ambit: a state-of-the-art in-memory computing mechanism
Evaluated SIMDRAM configurations (all using a DDR4_2400_x64 device):
  1-bank: SIMDRAM exploits 65’536 SIMD lanes (an 8 kB row buffer)
  4-banks: SIMDRAM exploits 262’144 SIMD lanes
  16-banks: SIMDRAM exploits 1’048’576 SIMD lanes
Notes: 5. Evaluation

## Slide 23: Methodology: Workloads
Evaluated:
16 complex in-DRAM operations:
  Absolute - Predication
  Addition/Subtraction - ReLU
  BitCount - AND-/OR-/XOR-Reduction
  Equality/ Greater/Greater Equal - Division/Multiplication
7 real-world applications
  BitWeaving (databases) - LeNET (neural networks)
  TPH-H (databases) - VGG-13/VGG-16 (neural networks)
  kNN (machine learning) - Brightness (graphics)

## Slide 24: Throughput Analysis
Chart: Average Normalized Throughput (GOPS/s) -- log scale
| CPU | GPU | Ambit
SIMDRAM - 1 Bank | 5.5 | 0.36 | 1.98
SIMDRAM - 4 Banks | 22 | 1.5 | 7.9
SIMDRAM - 16 Banks | 88.01 | 5.82 | 31.61
SIMDRAM significantly outperforms
all state-of-the-art baselines for a wide range of operations
Average normalized throughput across all 16 SIMDRAM operations

## Slide 25: Energy Analysis
Average normalized energy efficiency across all 16 SIMDRAM operations
Chart: Average Energy Efficiency (GOPS/s/Watt) -- log scale
| CPU | GPU | Ambit
SIMDRAM - 1 Bank | 257 | 31 | 2.6
SIMDRAM - 4 Banks | 257 | 31 | 2.6
SIMDRAM - 16 Banks | 257 | 31 | 2.6
SIMDRAM is more energy-efficient than
all state-of-the-art baselines for a wide range of operations

## Slide 26: Real-World Applications
Chart: Average Speedup -- log scale
| CPU | GPU | Ambit
SIMDRAM - 1 Bank | 3 | 0.30612 | 2.5
SIMDRAM - 4 Banks | 8.7 | 0.88776 | 7.25
SIMDRAM - 16 Banks | 21 | 2.1429 | 17.5
SIMDRAM effectively and efficiently accelerates
many commonly-used real-world applications
Average speedup across 7 real-world applications

## Slide 27: More in the Paper
Evaluation:
  Reliability
  Data transposition overhead
  Area overhead
  Comparison to in-cache computing
  And more …

## Slide 28
SIMDRAM: An end-to-end processing-using-DRAM framework that provides the programming interface, the ISA, and the hardware support for:
  Efficiently computing complex operations
  Providing the ability to implement arbitrary operations as required
  Using a massively-parallel in-DRAM SIMD substrate
Key Results: SIMDRAM provides:
  88x and 5.8x the throughput and 257x and 31x the energy efficiency of a baseline CPU and a high-end GPU, respectively, for 16 in-DRAM operations
  21x and 2.1x the performance of the CPU and GPU for seven real-world applications
Conclusion: SIMDRAM is a promising PuM framework
  Can ease the adoption of processing-using-DRAM architectures
  Improve the performance and efficiency of processing-using-DRAM architectures
Conclusion
Notes: 6. Conclusion

## Slide 29
Thank you
Prensented by:张梦豪
S211000834