## Slide 1: Designing Vertical Processors in Monolithic 3D
Mohammed Baabou LY2021037

## Slide 2: CONTENTS OF THIS PRSENTATION
BRIEF INTRODUCTION ABOUT THE PAPER
3D MONOLITHIC INTEGRATION AND COMPARISON M3D to TSV3D
PARTITIONING A CORE IN M3D
HETERO-LAYER PARTITIONING
ARCHITECTURES ENABLED BY M3D
EVALUATION SETUP

## Slide 3: BRIEF INTRODUCTION ABOUT THE PAPER 01

## Slide 4
Authors : Josep Torrellas , Bhargava Gopireddy
Institution : Saburo Muroga Professor of Computer Science
University of Illinois at Urbana-Champaign
He is the Director of the Center for Programmable Extreme-Scale
Computing, a Co-Leader of the Intel Strategic Research Alliance (ISRA)
On Computer Security, and past Director of the Illinois-Intel Parallelism
Center(I2PC).
Torrellas has made many contributions to shared-memory
Multiprocessor architectures and thread-level speculation (TLS) over
more than thirty years.

## Slide 5: 3D MONOLITHIC INTEGRATION AND COMPARISON M3D to TSV3D 02

## Slide 6: 3D MONOLITHIC
Monolithic 3D (M3D) [6, 8, 14] is a 3D integration technology that
allows high-bandwidth communication across layers and ultra
high density integration. Rather than bonding together pre-fabricated
dies as in TSV3D, an M3D chip is built by sequentially fabricating multiple layers of devices on top of one another.
Using M3D to build vertical processors is attractive for three
reasons. First, the active layers in M3D are separated by a distance
of less than 1μm, which is one to two orders of magnitude shorter
than in TSV3D [5, 20, 22]. Such short distance reduces the communication
latency between the layers of a processor and allows for
very compact designs.

## Slide 7
This work is the first one to show how to partition a processor
for M3D. We design a vertical processor by taking logic, storage,
and mixed logic-storage pipeline stages, and partition each of them
into two layers. Our partition strategy is aware of the fact that the
top layer has lower-performance transistors..
With conservative assumptions on M3D technology, our M3D
core executes applications on average 25% faster than a 2D core,
while consuming 39% less energy. With aggressive technology assumptions,
the M3D core is on average 38% faster than a 2D core and
consumes 41% less energy. Further, under a similar power budget,
an M3D multicore can use twice as many cores as a 2D multicore,
executing applications on average 92% faster with 39% less energy.
Finally, the M3D core is thermally efficient.

## Slide 8: 3D MONOLITHIC INTEGRATION
The integration process is fundamentally different from the conventional
3D integration, where dies are pre-fabricated and later
connected using TSVs. For this reason, M3D is also referred to as
sequential 3D, while TSV3D is known as parallel 3D. Figure 1 shows
a cross-section of an M3D stack. When the chip is placed on the
board, the heat sink is at the top. The layers of an M3D stack are
connected by Monolithic Inter-layer Vias (MIVs).
Figure 2 shows the relative area of an FO1 inverter, an MIV, an
SRAM bitcell, and a TSV at 15nm technology. An MIV uses 0.07x the
area of the inverter, while a TSV uses 37x the area of the inverter.

## Slide 10: Comparing M3D to TSV3D
Table 1 compares the area overhead of an MIV and a TSV to a 32-bit adder and a 32-bit SRAM cell at 15nm technology. The areas of the adder and SRAM cell are obtained from Intel. Note that, because an MIV is so small, it is assumed to be a square. For the TSV, we consider both our aggressive design with a 1.3μm diameter, and the most recent TSV design produced in research, which has a 5μm diameter. For the TSV, we add the area of the Keep Out Zone (KOZ) around it; for the MIV, there is no need for a KOZ.

## Slide 11
Thermal Properties. TSV3D stacks have die-to-die (D2D) layers in between the dies. Such layers have ≈13-16x higher thermal resistance than metal and silicon layers [1]. Therefore, vertical
thermal conductance is relatively limited in TSV3D, and there are substantial temperature differences across layers.
M3D integration requires only a few metal layers in the bottom layer, as they route mostly local wires. Hence, the two active layers in M3D are physically close to each other — typically less than 1μm apart, even with 3-4 metal layers [2, 25]. Therefore, thermal coupling between the layers is high. In addition, the inter-layer dielectric is only 100nm thick.

## Slide 12: PARTITIONING A CORE IN M3D 03

## Slide 13: Logic Stages
These wires comprise most of the intra-stage critical path wire delay. To optimize these wires, the best approach is to use CAD tools for place and route. It has been shown that 3D floor-planners customized for M3D integration reduce the lengths of local wires by up to 25% . There is little scope for further optimization of local wires using micro-architectural insights.
Semi-global wires connect one logic block to another logic block within a stage. These wires are often critical to performance from a micro-architectural viewpoint. M3D integration of a pipeline stage can reduce the footprint of the stage by up to 50% — in this case reducing the distance traversed
by the semi-global wires by up to 50%. Like in Black et al. we estimate that a 3D organization reduces the latency of the load to use and branch misprediction notification paths, possibly saving one cycle or more in each path.

## Slide 14: Logic Stages
Global wires span a significant section of the chip and may take multiple clock cycles. The global footprint reduction reduces the length of a global wire. An example of global wire is a link in a Network-on-Chip (NoC). If we manage to fold each core into about half of its original area, two cores can share a single NoC router stop
To verify the impact of wire length reduction in logic stages, we synthesize and lay out a 64-bit adder along with a bypass path in 45nm technology. We use the M3D place and route tools developed by Lim et al. The results show that a two-layer M3D implementation achieves a 15% higher frequency. Moreover, the footprint reduction observed is 41%

## Slide 15: Storage Structures
The storage structures in a core consist of SRAM structures such as
the register file and branch prediction table, and CAM structures
such as the issue queue and load/store queue. CAM and RAM structures
are structurally very similar in their layout. Therefore, we
treat them similarly for the purpose of partitioning them in 3D.
Bit Partitioning
BP spreads half of each word in each
layer, and places a driver in each layer. As a result, the effective
length of each word line is halved. Each word requires a via across
the layers (Figure 3(a)). Table 3 shows the percentage of improvement
we attain by bit partitioning our two structures using M3D
and TSV3D, compared to a 2D structure.

## Slide 16: Storage Structures
Word Partitioning (WP). WP spreads half of the words in each
layer, and places a driver in each layer. As a result, the effective
length of each bitline is halved. The number of vias needed is equal
to the array width (Figure 3(b)). Table 4 shows the percentage of
improvement we attain by word partitioning our two structures
using M3D and TSV3D, compared to a 2D structure.

## Slide 17: Storage Structures
Port Partitioning (PP). PP places the SRAM bit cell with half
of its ports in one layer and the rest of the ports with their access
transistors in the second layer. It needs two vias per SRAM bit cell as
shown in Figure 3(c). Table 5 shows the percentage of improvement
we attain by port partitioning our two structures using M3D and
TSV3D, compared to a 2D structure.

## Slide 18: HETERO-LAYER PARTITIONING 04

## Slide 19
Low temperature processing of the top layer in M3D causes the top
layer to have lower performance than the bottom one. As indicated
in Section 2.4.2, Shi et al. [45] found that the delay of an inverter in
the top layer is 17% higher than in the bottom one. Consequently,
we modify the core partitioning algorithms of Section 3 to alleviate
the impact of the slowdown. With these algorithms, we design a
hetero-layer M3D core.

## Slide 20: Logic Stages
In storage structures, the critical path spans the entire array.
Hence, we cannot use the same approach as for the logic. Instead,
we use two separate techniques based on the partitioning strategy
applied in Section 3.2. Specifically, in port partitioning, we exploit
the fact that the two inverters in the SRAM bit cell are in the bottom
layer
Partitioning an Integer Execution Unit. Figure 5 shows a 64-
bit carry skip adder. The critical path is shown shaded. It consists
of a carry propagate block, a sum block, 15 mixes and a final sum
block

## Slide 21
Partitioning Decode. Modern x86 processors have a set of
simple decoders and a complex decoder. Most common instructions
that translate into a single μop are processed by the simple decoders.

## Slide 22: Storage Structures
Port Partitioning (PP). As shown in Table 6, PP is the best
strategy for multipored arrays such as the RF, IQ, SQ, LQ, and
RAT. In a port-partitioned cell, the two inverters are left in the
bottom layer, while the ports are divided between the two layers. In

## Slide 23: ARCHITECTURES ENABLED BY M3D 05

## Slide 24
Alternatively, one can increase the sizes or the number of ports
for some of the storage structures, while maintaining the same
frequency as a 2D core. Note that most of the structures that are
bottlenecks in wide-issue cores benefit significantly from M3D.
They include multi-ported issue queues, multi-ported register files,
and bypass networks. Therefore, one can increase the issue width
of the core while maintaining the same frequency.
Hetero M3D design. We have partitioned a core assuming heterogeneous M3D layers. However, it is possible that, in the future,
M3D may support same-performance layers. Even in this case, our
partitioning techniques may be applicable.

## Slide 25: EVALUATION SETUP 04

## Slide 26
We consider performance, energy, and thermals in turn.
Single Core M3D Designs
Figure 6 shows the speed-up of different single core M3D designs over Base for SPEC2006 applications. The figure shows a set of bars for each application and the average. For each application, there is a bar for Base, TSV3D, M3D-Iso, M3D-HetNaive, M3D-Het, and M3D-HetAgg. The bars are normalized to Base. M3D-Iso, where both layers have the same performance, is on average 28% faster than Base. The performance improvement is due to two reasons. First, M3D-Iso executes at a 16% higher frequency than Base.

## Slide 27
Single Core M3D Designs
Energy. Figure 7 shows the energy consumption of different M3D designs normalized to Base. The designs considered and the organization of the figure are the same as in Figure 6. We can see that all of the M3D designs consume, on average, about 40% less energy than Base. This is due to a few factors. First, as shown in Table 6, the energy consumption of many SRAM structures is significantly smaller. Second, the footprint of the clock tree network is only about half that of Base. Finally, M3D designs execute faster, saving leakage power on top of the previous reductions.

## Slide 28
Single Core M3D Designs
Multicores with Four Cores. M3D-Het, M3D-Het-W, and TSV3D have four cores. On average, we see that M3D-Het provides a speedup of 1.26 over Base, while reducing energy consumption by 33%. The performance gains include the benefits of shared L2s and NoC router on top of the gains seen in the single-core environment. With respect to the energy, we observe a slight reduction in dynamic energy due to the reduction in the network traffic, in addition to the energy saving factors discussed previously.

## Slide 29
Single Core M3D Designs
Iso Power Environment. M3D-Het-2X is an M3D-Het design operating at the same frequency as Base, but at a lower voltage and thus with lower power. As a result, it has twice as many cores as Base with about the same power budget as Base. From Figure 9, we see that M3D-Het-2X is 92% faster the Base.

## Slide 30
THANKS